## Slide 1
HTCommander · Signal Processing
DART
Data Adaptive Rate Transport
A coherent, adaptive OFDM modem for sending data through
ordinary FM voice radios over a Bluetooth (SBC) audio link.
DFT-spread OFDM
LDPC FEC
Adaptive 1–6 kbps
Validated over the air
How the protocol works — encoding & decoding pipeline, end to end

## Slide 2
MOTIVATION
The problem: data over an FM voice channel
▸ Ham handhelds give you a voice channel — not a data port.
  – To move data you must encode it as audio the radio will pass.
▸ Legacy modes are slow.
  – AFSK 1200 bps and PSK 2400 bps are the common options.
▸ The path is genuinely hostile to data.
  – FM audio + AGC + limiter + companding distort amplitude & phase.
  – On modern radios audio rides a Bluetooth SBC codec — twice.
▸ Goal: 1–6 kbps that degrades gracefully, not a cliff.
The real-world signal chain
app ──PCM──▶ Bluetooth SBC ──▶ radio TX
│
FM over air
▼
app ◀──PCM── Bluetooth SBC ◀── radio RX
Every frame crosses the lossy SBC
codec TWICE — once on each hop.
DART must survive all of it and
still verify every byte with a CRC.
2
DART — Data Adaptive Rate Transport

## Slide 3
CHANNEL MODEL
What the FM-over-SBC channel actually looks like
Property | Behavior
Sample rate | 32 kHz, 16-bit, mono PCM
Usable band | ~400–2600 Hz (flat within ~2 dB)
Unusable | < 300 Hz (AC-coupled), > 3000 Hz (SBC rolloff)
Channel type | Static band-pass — no fading, no multipath
Amplitude | Mildly compressed (AGC + limiter + SBC)
Noise floor | FM noise + SBC quantization; SNR ~20–25 dB
Delay spread | Negligible (< 125 µs)
▸ The channel is STATIC.
  – One training preamble is enough to estimate & equalize it.
  – No continuous adaptive equalizer needed.
▸ The real enemy is time-varying phase, not the band shape.
  – A static response is removed by the equalizer.
  – Carrier phase noise is what limits the dense modes.
3
DART — Data Adaptive Rate Transport

## Slide 4
DESIGN
Five ideas that make DART work
1
DFT-spread OFDM
Frequency-domain equalization with single-carrier-low PAPR. Puts energy only in the usable 400–2600 Hz band.
2
Adaptive rate ladder
Seven modes (BPSK→16QAM + FSK). Each frame is self-describing, so the link trades speed for robustness on the fly.
3
LDPC forward error correction
Soft-decision belief-propagation decoding. Four code rates (1/2 → 5/6) matched to the modulation.
4
Self-describing frames
A robust mode-0 header lets ANY receiver decode any frame with no prior negotiation — broadcast & monitoring work.
5
Constant-envelope fallback
Mode F (4-FSK) is immune to amplitude distortion — the guaranteed-delivery floor when nothing else survives.
4
DART — Data Adaptive Rate Transport

## Slide 5
WAVEFORM
Why DFT-spread OFDM (SC-FDMA)
▸ OFDM: many slow subcarriers across the band.
  – Turns a frequency-selective channel into flat per-bin gains.
  – Equalization is a single complex divide per subcarrier.
▸ DFT-spread = SC-FDMA precoding.
  – Spreads each symbol across all tones before the IFFT.
  – Restores single-carrier-like low PAPR → less limiter crush.
▸ Measured PAPR reduction: ~1.3–2.0 dB vs plain OFDM.
  – Headroom against the FM limiter / AGC.
Constellation | Plain OFDM | SC-FDMA
BPSK | 10.5 dB | 8.5 dB
QPSK | 10.7 dB | 8.8 dB
8PSK | 10.7 dB | 8.8 dB
16QAM | 10.6 dB | 9.3 dB
99th-percentile peak-to-average power ratio.
Lower PAPR = the waveform's peaks are closer to its average, so the radio's limiter clips it less.
5
DART — Data Adaptive Rate Transport

## Slide 6
PARAMETERS
OFDM physical-layer parameters
Parameter | Value
Sample rate | 32 kHz, 16-bit, mono
FFT size | 128
Subcarrier spacing | 250 Hz (32 kHz / 128)
Active subcarriers | 9 (bins 2–10, ≈500–2600 Hz)
Cyclic prefix | 4 samples = 125 µs
Guard padding | 256 samples each side (~2 SBC frames)
Spectrum occupancy
freq (Hz) 0 500 2600 3000 ... 16000
│░░░░░│█████████│░░░░░░│
AC- 9 active SBC
coup. carriers rolloff
Only 9 FFT bins carry data — exactly the
part of the band the radio passes cleanly.
Short CP (125 µs) is a deliberate bet:
FM at these ranges has ~no multipath, so
a long CP would just waste airtime.
6
DART — Data Adaptive Rate Transport

## Slide 7
FRAMING
Frame structure
Guard
Zadoff-Chu
preamble
Header
(mode 0)
Payload
(variable mode)
Guard
Preamble — Zadoff-Chu (root 7, len 127) + 1 channel-estimation symbol. Constant-envelope, same for every mode.
Header — ALWAYS mode 0 (BPSK R1/2), so any receiver can read it regardless of link quality.
Payload — modulated & coded per the mode index in the header.
Guard — 256 samples so the SBC filterbank warms up & flushes without corrupting the frame.
Header field | Bits
Mode index (0–5, F) | 4
Payload length (bytes) | 12
Source callsign (AX.25) | 48
Destination callsign | 48
Sequence number (ARQ) | 8
Flags (ACK/NACK/data/bcast) | 8
Header CRC-16 | 16
7
DART — Data Adaptive Rate Transport

## Slide 8
RATE LADDER
The adaptive mode table
Mode | Constellation | LDPC rate | Bits/sym | Net throughput | Role
0 | BPSK | 1/2 | 1 | ~1 kbps | most robust
1 | QPSK | 1/2 | 2 | ~2 kbps | robust
2 | QPSK | 2/3 | 2 | ~3 kbps | real-link ceiling
3 | 8PSK | 2/3 | 3 | ~4 kbps | needs ~13 dB SNR
4 | 16QAM | 3/4 | 4 | ~5 kbps | needs ~16 dB SNR
5 | 16QAM | 5/6 | 4 | ~6 kbps | fastest
F | 4-CPFSK | 1/2 | ~1 | ~0.4 kbps | constant-envelope floor
▸ Modes 0–5 share ONE OFDM modulator/demodulator — only the constellation lookup and LDPC rate change.
▸ Mode F uses a separate constant-envelope FSK modulator but shares the header, LDPC, interleaver, scrambler, CRC and ARQ.
8
DART — Data Adaptive Rate Transport

## Slide 9
ENCODING
Transmit pipeline — bytes to PCM
1. Payload bytes
the AX.25 frame to send
2. Append CRC-32
integrity check over the payload
3. LDPC encode
systematic [data | parity], rate per mode
4. Interleave
block interleave — break SBC burst errors
5. Scramble (PN15)
whiten coded bits → flat spectrum, low PAPR
6. Constellation map
BPSK / QPSK / 8PSK / 16QAM (Gray-coded)
7. DFT-spread + OFDM
SC-FDMA precode → IFFT → cyclic prefix
8. Assemble frame
preamble + header + payload + guard
9. 32 kHz PCM out
to the radio over Bluetooth SBC
9
DART — Data Adaptive Rate Transport

## Slide 10
DECODING
Receive pipeline — PCM back to bytes
1. 32 kHz PCM in
rolling buffer of samples from the radio
2. Detect preamble
Zadoff-Chu correlation → frame start + timing
3. Estimate channel
H[k] = Y/X per subcarrier from the preamble
4. Decode header
always mode 0 (BPSK R1/2) → mode, length, calls
5. Refine channel
re-encode header as extra pilots → kills SBC phase err
6. Demodulate payload
FFT → MMSE equalize → de-spread → pilots track phase
7. Soft demap (LLRs)
per-bit log-likelihood ratios
8. Descramble + deinterleave
undo PN15 (sign-flip LLRs) + reorder
9. LDPC soft decode
min-sum belief propagation, ≤ 50 iterations
10. CRC-32 check
verified payload → dispatch as a frame
10
DART — Data Adaptive Rate Transport

## Slide 11
FORWARD ERROR CORRECTION
LDPC — the error-correcting core
▸ IEEE 802.11n information-part connections, N = 648.
▸ Dual-diagonal (IRA accumulator) parity structure.
  – O(M) systematic encoding at every rate — always succeeds.
▸ Soft-input decoder: min-sum belief propagation.
  – Input is LLRs: positive → likely 0, negative → likely 1.
  – Iterative check/variable-node message passing, ≤ 50 iters.
  – 0.75 scaling factor on the min-sum approximation.
▸ Code shortening on short frames (next slide) adds 5+ dB.
Rate | K (info) | N (coded) | Modes
1/2 | 324 | 648 | 0, 1, F
2/3 | 432 | 648 | 2, 3
3/4 | 486 | 648 | 4
5/6 | 540 | 648 | 5
Systematic code: the K information bits appear verbatim in the codeword, followed by N−K parity bits.
11
DART — Data Adaptive Rate Transport

## Slide 12
WHITENING
Scrambling — why the modem randomizes its own bits
▸ Repetitive data (a frame of zeros) is poison for QAM.
  – Spectral lines, PAPR blows up, constellation collapses.
  – Phase/timing recovery starve on a DC-like stream.
▸ LDPC can't fix it — it's linear.
  – All-zero input → all-zero codeword. Interleaver just shuffles zeros.
▸ So scramble AFTER LDPC + interleave, before the mapper.
▸ Additive PN15 LFSR, reset per frame.
  – x¹⁵ + x¹⁴ + 1, period 32,767 > largest frame's coded bits.
  – 1 channel error stays 1 error (no multiplication like G3RUH).
  – RX descramble = conditional LLR sign-flip — lossless to FEC.
Where it slots in
TX: ... interleave → [SCRAMBLE] → map ...
RX: ... soft-demap → [DESCRAMBLE] →
deinterleave ...
Scrambler | Error behavior | Soft FEC
Multiplicative | multiplies ×(taps+1) | corrupts LLRs
Additive (DART) | 1 error → 1 error | clean sign-flip
12
DART — Data Adaptive Rate Transport

## Slide 13
RECEIVER TRICK
Code shortening — free margin on short frames
▸ A short message fills only part of a fixed LDPC block.
  – The rest is zero-padding — bits whose value we already know.
▸ Tell the decoder those bits are known (pin their LLRs).
  – Known bits become CONSTRAINTS that tighten parity checks.
  – The effective code rate collapses → recovers from noisier input.
▸ Purely a smarter receiver — nothing on air changes.
  – Also strengthens the 144-bit header inside its 324-bit block.
▸ Self-scaling: biggest gain on the shortest frames (ACKs, beacons).
16QAM R5/6, 2-byte frame | Decodes to
Without shortening | +3 dB SNR
With shortening | −2 dB SNR
> 5 dB improvement.
The failure mode even changes: the LDPC code is no longer the bottleneck — the preamble detector gives out first.
13
DART — Data Adaptive Rate Transport

## Slide 14
SYNC
Synchronization & channel estimation
Preamble detection
Cross-correlate against the known Zadoff-Chu sequence. Ideal autocorrelation (zero sidelobes) → a sharp, unambiguous peak marks frame start.
Frequency offset
The preamble's repeated halves rotate in phase by Δf·T. The angle between them gives the carrier frequency offset, corrected by a complex de-rotation.
Channel estimation
Divide the received preamble spectrum by the known transmitted one: H[k] = Y[k] / X[k] at every active subcarrier. One shot — the channel is static.
Equalization
One complex tap per subcarrier. MMSE: X̂ = H*·Y / (|H|² + σ²) — limits noise blow-up on weak subcarriers vs plain zero-forcing.
14
DART — Data Adaptive Rate Transport

## Slide 15
KEY RESULT
Surviving the Bluetooth SBC codec
▸ The single hardest problem: the SBC codec round-trip.
  – Left ~29° residual phase error after one channel estimate.
  – BPSK tolerated it; QPSK and above failed CRC.
▸ Fix: decision-directed channel refinement.
  – The header always decodes (sent at the most robust mode).
  – Re-encode it → treat its 72 OFDM symbols as extra pilots.
  – Average Y·conj(X) across them → far better phase estimate.
▸ Result: every higher-order mode survives the SBC codec.
Measured
SBC probe (real UV-Pro hardware):
group delay ........ ~73 samples
preamble corr ...... ~0.89 (preserved)
residual phase ..... 29° → tracked out
The guard interval absorbs the 73-sample
delay; correlation stays well above the
0.6 detection threshold.
TX stream raised to bitpool 40 (from 18);
radio→app return path fixed at 18 by
firmware.
15
DART — Data Adaptive Rate Transport

## Slide 16
CHASING THE CEILING
Phase noise & pilot-aided tracking
▸ Over the air, dense modes failed worse than simulation predicted.
  – The culprit: time-varying carrier phase noise.
▸ Two regimes that look identical on an EVM meter:
  – Fast (> ~12°/sym): inter-carrier interference — irreducible.
  – Slow (drifts across the frame): correctable with pilots.
▸ Pilots: known symbols every 8 data symbols.
  – Give a decision-independent phase reference.
▸ Measured real link: 0.5–1.6°/symbol → slow regime.
  – Pilots recovered QPSK R2/3: +50% throughput (~2 → ~3 kbps).
Phase drift | With pilots | No pilots
~12°/sym (fast) | fail | fail
~5°/sym | 14.5% | 17.0%
~2.6°/sym (slow) | 9.6% | 14.5%
16QAM EVM at fixed noise. Pilots win when phase is slow, do nothing when it's fast.
Remaining 8PSK/16QAM ceiling is raw SNR — a link-budget problem, not DSP.
16
DART — Data Adaptive Rate Transport

## Slide 17
VERIFIED
Inter-symbol interference & the cyclic prefix
▸ The CP is a guard buffer against channel echoes.
  – Echo within CP → equalizer folds it in, invisibly.
  – Echo beyond CP → energy spills: inter-symbol interference.
▸ DART's CP is deliberately short: 4 samples = 125 µs.
▸ Measured: clean knee exactly at the CP boundary.
  – EVM roughly doubles the moment an echo exceeds 4 samples.
▸ Real SBC/audio path adds NO dispersion past the CP.
  – Growing the CP through SBC buys nothing — flat 0.4% EVM.
  – RF multipath would need a ~37 km path difference to matter.
Echo delay | In time | EVM
4 samples (= CP) | 125 µs | 4.2%
5 samples (> CP) | 156 µs | 7.9%
8 samples | 250 µs | 11.3%
16 samples | 500 µs | 14.9%
Verdict: the short-CP bet was safe. ISI is not a DART limiter.
17
DART — Data Adaptive Rate Transport

## Slide 18
FALLBACK
Mode F — the constant-envelope floor
▸ For amplitude-hostile radios (hard limiting, companding).
▸ 4-CPFSK: one of four continuous-phase tones per symbol.
  – Strictly constant envelope → immune to AGC/limiter/SBC amplitude damage.
  – Non-coherent detection — no channel estimate or phase tracking.
▸ Whole frame (header + payload) is FSK → amplitude-immune end to end.
▸ Shares LDPC, interleaver, scrambler, CRC and ARQ with the OFDM modes.
▸ Cost: ~3× longer on air — the bottom rung of the ladder.
Parameter | Value
Modulation | 4-CPFSK, 2 bits/sym
Symbol rate | 400 symbols/s
Tones | 600/1000/1400/1800 Hz
FEC | LDPC rate 1/2
When nothing else works
8% hard-clip + SBC + 14 dB SNR:
16QAM modes ...... 0/5 decoded
Mode F (4-FSK) ... 5/5 decoded
18
DART — Data Adaptive Rate Transport

## Slide 19
LINK LAYER
Delivery: datagrams, ARQ & rate adaptation
Connectionless datagrams
Fire-and-forget with the broadcast flag. No ACK. The right model for APRS beacons, group chat, and CQ calls — the packet goes to everyone.
Connected ARQ
Sliding send window (default 4 in flight). In-order delivery, ACK per good frame, NACK + selective retransmit of only the lost frame. Keeps the pipe full.
Rate adaptation
Walks the ladder F→0→1→2→3→4→5: up one rung after 3 clean ACKs, down two on any NACK/timeout. Same MCS idea as Wi-Fi, LTE, VARA.
Per-packet metadata
Every frame records direction, mode, EVM, SNR, preamble correlation, retransmits, CRC — the rows the Flutter packet-capture tab renders.
19
DART — Data Adaptive Rate Transport

## Slide 20
FIELD RESULTS
Over the air: two UV-Pro HTs, 50 ft, 2 m / 70 cm
Level | Mode | EVM | SNR | Phase drift | CRC
0 | BPSK R1/2 | ~45% | ~7 dB | 1.6°/sym | OK
1 | QPSK R1/2 | ~42% | ~7.5 dB | 1.3°/sym | OK
2 | QPSK R2/3 | ~44% | ~7 dB | 1.4°/sym | OK
3 | 8PSK R2/3 | ~34% | ~9.4 dB | 0.6°/sym | fail
4 | 16QAM R3/4 | ~28% | ~11 dB | 0.9°/sym | fail
▸ Reliable ceiling: Level 2, ~3 kbps.
▸ Textbook graceful degradation.
▸ Phase noise solved by pilots.
▸ 8PSK/16QAM are SNR-limited — a link-budget problem.
▸ Mode F delivered through an 8% hard-clip channel.
Simulation control experiment: 16QAM through simulated SBC + 25 dB noise decoded at 2.9% EVM with zero corrections —
proving the over-the-air failure is the radio's phase noise, not the codec or additive noise.
20
DART — Data Adaptive Rate Transport

## Slide 21
SOURCE MAP
Where it lives in the code (src/lib/hamlib/)
dart_modem.dart
Full TX/RX chain, frame & header, 6-mode table, channel refinement
dart_ofdm.dart
OFDM + DFT-spread, radix-2 FFT/IFFT, CP, equalizer
dart_constellation.dart
BPSK/QPSK/8PSK/16QAM map & soft-LLR demap; Complex type
dart_ldpc.dart
LDPC encoder + min-sum belief-propagation soft decoder
dart_fsk.dart
Constant-envelope 4-CPFSK modem for Mode F
dart_preamble.dart
Zadoff-Chu preamble: detection, sync, channel estimation
dart_link.dart
Link layer: datagrams, selective-repeat ARQ, rate adaptation
dart_packet_info.dart
Per-packet metadata & signal quality for the capture tab
Integrated via software_modem.dart (Audio → Software Modem → DART) — rides the same 32 kHz broker flow as AFSK 1200 and PSK 2400.
21
DART — Data Adaptive Rate Transport

## Slide 22
SUMMARY
DART in one slide
▸ Adaptive DFT-spread OFDM + LDPC for FM voice radios.
▸ 9 subcarriers in 400–2600 Hz; 32 kHz / 16-bit mono.
▸ Seven self-describing modes: BPSK → 16QAM, plus 4-FSK floor.
▸ Robust mode-0 header → any receiver decodes any frame.
▸ Decision-directed refinement + pilots beat SBC phase noise.
▸ Scrambling, code shortening, MMSE, short CP — all measured.
▸ Link layer: datagrams, selective-repeat ARQ, rate ladder.
~3 kbps
reliable over-the-air ceiling (QPSK R2/3)
6 modes
all pass encode→SBC→noise→decode in test
5+ dB
margin from code shortening on short frames
0.5–1.6°/sym
real-link phase drift — tracked by pilots
22
DART — Data Adaptive Rate Transport